## Slide 1
SUB-NATIONAL E-WASTE SERIES · INDIA
E-Waste It Wisely at the
Sub-National Level
A District-Level Assessment of Generation, Collection & Recycling
Performance in Sikkim, India — FY 2026
Six districts. One dashboard. A 5.9% capture rate against 310.5 tonnes
generated — the same collection-infrastructure gap documented across
other developing regions, now visible at state scale.
Tanmay Lalge · Yukta Padekar
Vidyalankar Institute of Technology, Mumbai
SIKKIM · SIX DISTRICTS
Mangan
no recycler
28.0 t
Gangtok
39% of state
120.0 t
Gyalshing
no coverage
52.5 t
Pakyong
recycler present
31.5 t
Namchi
recycler present
52.5 t
Soreng
no recycler
26.0 t
Source: Sikkim State Pollution Control Board, E-Waste Management Dashboard, FY 2026
1

## Slide 2
The Capture Gap
Regulation and reporting are mature; formal collection is not
THE SHORTFALL
310.5 t
generated statewide in FY 2026, across all six districts
18.2 t (5.9%)
formally collected — a roughly 17-to-1 generation-to-collection gap
Even Gangtok — the best-resourced district — captures only 6.8% of its own generation. Sikkim's 5.9% statewide capture rate sits well below the 17.4% global average reported for 2019.
THE OPENING
1,100 t/yr
installed recycling capacity across 3 authorised facilities
83.9%
EPR achievement against target — 12 of 20 producers fully compliant
Installed capacity already exceeds total generation, and recyclers run at only 63% utilisation. The binding constraint is upstream collection, not downstream processing — a logistics problem, not an engineering one.
Synthesis: Sikkim's constraint is not legislative absence — it is weak collection infrastructure, uneven district coverage, and limited informal-sector formalisation.
Source: Sikkim SPCB E-Waste Management Dashboard, FY 2026
2

## Slide 3
The District Divide
Gangtok concentrates generation, recyclers, and outreach; three districts have none of the three
GENERATED vs. COLLECTED (TONNES)
Chart: Tonnes
| Gangtok | Namchi | Gyalshing | Pakyong | Mangan | Soreng
Generated (t) | 120 | 52.5 | 52.5 | 31.5 | 28 | 26
Collected (t) | 8.2 | 4.7 | 2.6 | 3.3 | 0.9 | 1.3
CAPTURE RATE & COVERAGE
District | Capture | Recycler | Outrch.
Gangtok | 6.8% | Yes | Yes
Namchi | 9.0% | Yes | Yes
Pakyong | 10.5% | Yes | No
Gyalshing | 5.0% | No | No
Soreng | 5.0% | No | Yes
Mangan | 3.2% | No | No
Gangtok alone generates 39% of the state total. Gyalshing, Mangan, and Soreng have no authorised recycler; Gyalshing and Mangan have received no awareness programme at all.
Source: Sikkim SPCB E-Waste Management Dashboard, FY 2026 — Table I
3

## Slide 4
Anatomy of the Waste Stream
What Sikkim throws away, and who is licensed to process it
GENERATION MIX BY CATEGORY
Chart: 
| Large/small equip. | IT & telecom | Consumer electronics | Batteries | Lighting | Other
Share | 33 | 27 | 23 | 9 | 4 | 4
Large/small equip. — 33%
IT & telecom — 27%
Consumer electronics — 23%
Batteries — 9%
Lighting — 4%
Other — 4%
Large & small equipment — bulkier, more hazardous, least likely to be captured informally — is the single largest category.
AUTHORISED RECYCLERS
Facility | District | Cap. (t/yr) | Processed | Recovery
Sikkim Eco Dismantlers | Gangtok | 500 | 320 t | 81%
Eastern Recyclers | Namchi | 350 | 210 t | 79%
Himalayan E-Waste Sol. | Pakyong | 250 | 160 t | 77%
1,100 t/yr capacity vs. 310.5 t generated
Combined utilisation is only ~63%. All three facilities sit in just three of six districts — Gyalshing, Mangan, and Soreng have none.
Source: Sikkim SPCB E-Waste Management Dashboard, FY 2026 — Table II
4

## Slide 5
The Human Toll
Informal labour still carries the system, and outreach hasn't reached everyone
INFORMAL WORKFORCE
42%
of 97 identified informal e-waste workers are registered or trained
Three hotspot clusters — MG Marg (Gangtok), Namchi Scrap Market, and Pakyong Repair Cluster — show similar 40–47% registration, so the gap is broad-based, not localised.
ENVIRONMENTAL HEALTH
1 of 3
monitored sites shows contamination — minor water impact at Pakyong
195 people screened at two health camps; no camp yet held at Namchi Scrap Market. Air and soil are within limits at the other two sites — a favourable, early-stage picture.
AWARENESS REACH
3 of 6
districts reached by an awareness campaign so far
1,580 people reached across three campaigns — led by an 850-person door-to-door drive in Gangtok. Gyalshing and Mangan have had no outreach at all.
Source: Sikkim SPCB E-Waste Management Dashboard, FY 2026 — Tables III & related
5

## Slide 6
Roadmap to Closing the Gap
Four priorities to move Sikkim from compliant on paper to captured in practice
1
Expand Collection
Add collection points beyond the current 8 centres, prioritising bulky large/small equipment — 33% of the stream and least likely to be captured informally.
2
Cover the Gaps
Bring recycling and outreach to Gyalshing, Mangan, and Soreng using shared or mobile collection points modelled on Gangtok's approach.
3
Formalise Labour
Register and train the 56 of 97 informal workers still uncovered, across all three hotspot clusters, with PPE included at registration.
4
Reconcile & Monitor
Explain the 83.9% EPR vs. 5.9% capture gap, run the outstanding Namchi health camp, and publish the dashboard quarterly instead of once.
Bottom line: Sikkim's recycling capacity, EPR reporting, and regulatory monitoring already work. Collection logistics — not new law or new plants — is the lever most likely to move the 5.9% capture rate.
6